## Slide 1: PID Line FOLLOWER
BY SANJAY AND ARVIND SESHAN

## Slide 2: Lesson Objectives
Learn the limitations of proportional control
Learn what PID means
Learn how to program PID and how to tune

## Slide 3: When does Proportional Control Have Trouble?
What would a human do?
On line  go straight
On white  turn left
Moving across line  turn right
On white  turn left
Getting further from line  turn even more!
What would proportional control do?
On line  go straight
On white  turn left
Moving across line  go straight!
On white  turn left
Getting further from line  turn left the same amount!
LIGHT READING =
50%
100%
Note: the following few slides are animated. Use PowerPoint presentation mode to view them

## Slide 4: How can we fix Proportional Control?
What would a human do?
Turning left/on line  turn right
Getting further from line  turn even more!
What would proportional control do?
Turning left/on line  go straight!
Getting further from line  turn left the same amount!
1. Predict what the next sensor reading will be
2. Has past steering fixes helped reduce error?

## Slide 5: Integrals and Derivatives
If readings are: 75, 65, 55  what do you think the next reading will be?
  What if the readings were 57, 56, 55…
What information did you use to guess?
Derivative  the rate at which a value is changing
When the correction is working well, what does error readings look like?
  +5, -6, +4 -3…. i.e. bouncing around 0
When steering is not working, what does error look like?
  +5, +5, +6, +5… i.e. always on one side of 0
How can we detect this easily?
  Hint: look at the sum of all past errors
What is an ideal value for this sum? What does it mean if the sum is large?
Integral  the “sum” of values
1. Predict what the next sensor reading will be?
2. Have past steering fixes helped reduce error?

## Slide 6: What is PID?
Proportional [Error]  How bad is the situation now?
Integral  Have my past fixes helped fix things?
Derivative  How is the situation changing?
PID control  combine the error, integral and derivative values to decide how to steer the robot

## Slide 7: Error
Solid line represents what you have seen, dotted line is the future
At time 20, you see light reading = 40 and error = -10 (red X)
Chart: Error
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Light Intensity | 0 | 6.7474 | 11.9856 | 15.7301 | 18.0315 | 18.9797 | 18.703 | 17.3645 | 15.155 | 12.2854 | 8.9771 | 5.4523 | 1.9244 | -1.4112 | -4.3848 | -6.8587 | -8.7323 | -9.9443 | -10.4735 | -10.3375 | -9.5892
 | -9.5892 | -8.3123 | -6.6144 | -4.6207 | -2.4654 | -0.28439 | 1.7927 | 3.649 | 5.1867 | 6.3314 | 7.035 | 7.2776 | 7.0668 | 6.4368 | 5.4442 | 4.1648 | 2.6877 | 1.1099 | -0.46969 | -1.9562 | -3.2641 | -4.3218 | -5.0752 | -5.4906 | -5.5555 | -5.279 | -4.6899 | -3.8351 | -2.7754 | -1.582 | -0.33161
Chart: Light Intensity
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Light Intensity | 50 | 56.7474 | 61.9856 | 65.7301 | 68.0315 | 68.9797 | 68.703 | 67.3645 | 65.155 | 62.2854 | 58.9771 | 55.4523 | 51.9244 | 48.5888 | 45.6152 | 43.1413 | 41.2677 | 40.0557 | 39.5265 | 39.6625 | 40.4108
 | 40.4108 | 41.6877 | 43.3856 | 45.3793 | 47.5346 | 49.7156 | 51.7927 | 53.649 | 55.1867 | 56.3314 | 57.035 | 57.2776 | 57.0668 | 56.4368 | 55.4442 | 54.1648 | 52.6877 | 51.1099 | 49.5303 | 48.0438 | 46.7359 | 45.6782 | 44.9248 | 44.5094 | 44.4445 | 44.721 | 45.3101 | 46.1649 | 47.2246 | 48.418 | 49.6684
Subtract target (50)

## Slide 8: Integral
Looks at past history of line follower
Sum of past error
Like area under the curve in graph (integral)
  Green = positive area
  Red = negative area
Chart: Time (sec)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Light Intensity | 0 | 6.7474 | 11.9856 | 15.7301 | 18.0315 | 18.9797 | 18.703 | 17.3645 | 15.155 | 12.2854 | 8.9771 | 5.4523 | 1.9244 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -1.4112 | -4.3848 | -6.8587 | -8.7323 | -9.9443 | -10.4735 | -10.3375 | -9.5892
Chart: Time (sec)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Light Intensity | 0 | 6.7474 | 18.733 | 34.4631 | 52.4947 | 71.4744 | 90.1774 | 107.5418 | 122.6968 | 134.9822 | 143.9593 | 149.4116 | 151.3359 | 149.9247 | 145.5399 | 138.6811 | 129.9488 | 120.0045 | 109.5309 | 99.1934 | 89.6042
 | 89.6042 | 81.2919 | 74.6775 | 70.0568 | 67.5913 | 67.3069 | 69.0996 | 72.7486 | 77.9354 | 84.2667 | 91.3017 | 98.5793 | 105.6461 | 112.0829 | 117.5271 | 121.692 | 124.3797 | 125.4896 | 125.0199 | 123.0637 | 119.7996 | 115.4778 | 110.4026 | 104.9121 | 99.3566 | 94.0776 | 89.3877 | 85.5526 | 82.7773 | 81.1953 | 80.8637

## Slide 9: Derivative
How quickly is position changing?
  Predicts where the robot will be in the immediate future
  Same as how fast is error changing
Can be measured using tangent line to measurements  derivative
  Approximated using two nearby points on graph
Chart: Time (sec)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Light Intensity | 0 | 6.7474 | 11.9856 | 15.7301 | 18.0315 | 18.9797 | 18.703 | 17.3645 | 15.155 | 12.2854 | 8.9771 | 5.4523 | 1.9244 | -1.4112 | -4.3848 | -6.8587 | -8.7323 | -9.9443 | -10.4735 | -10.3375 | -9.5892
 | -9.5892 | -8.3123 | -6.6144 | -4.6207 | -2.4654 | -0.28439 | 1.7927 | 3.649 | 5.1867 | 6.3314 | 7.035 | 7.2776 | 7.0668 | 6.4368 | 5.4442 | 4.1648 | 2.6877 | 1.1099 | -0.46969 | -1.9562 | -3.2641 | -4.3218 | -5.0752 | -5.4906 | -5.5555 | -5.279 | -4.6899 | -3.8351 | -2.7754 | -1.582 | -0.33161
Tangent line
Chart: Time (sec)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Light Intensity | 0 | 6.7474 | 5.2383 | 3.7445 | 2.3014 | 0.94817 | -0.27666 | -1.3386 | -2.2095 | -2.8696 | -3.3083 | -3.5248 | -3.5279 | -3.3356 | -2.9735 | -2.4739 | -1.8736 | -1.212 | -0.52921 | 0.13603 | 0.74827
 | 0.74827 | 1.277 | 1.6978 | 1.9937 | 2.1553 | 2.181 | 2.0771 | 1.8563 | 1.5377 | 1.1447 | 0.70361 | 0.24255 | -0.21071 | -0.63007 | -0.99254 | -1.2794 | -1.4771 | -1.5778 | -1.5796 | -1.4865 | -1.3079 | -1.0576 | -0.75341 | -0.41539 | -0.064947 | 0.27655 | 0.58903 | 0.85484 | 1.0597 | 1.1934 | 1.2504

## Slide 10: Pseudocode
Take a new light sensor reading
Compute the “error”
Scale error to determine contribution to steering update (proportional control)
Use error to update integral (sum of all past errors)
Scale integral to determine contribution to steering update (integral control)
Use error to update derivative (difference from last error)
Scale derivative to determine contribution to steering update (derivative control)
Combine P, I, and D feedback and steer robot

## Slide 11: Code - Proportional
This is the same as the proportional control code
Error = distance from line = reading - target
Correction (P_fix) = Error scaled by proportional constant (Kp) = 0.3
error = color.get_reflected_light() - 50
P_fix = error * 0.3

## Slide 12: Code - Integral
This section calculates the integral. It adds the current error to a variable that has the sum of all the previous errors.
The scaling constant is usually small since Integral can be large
Integral = sum of all past errors = last integral + newest error
Correction (I_fix) = Integral scaled by proportional constant (Ki) = 0.001
integral = integral + error # or integral+=error
I_fix = integral * 0.001

## Slide 13: Code - Derivative
This section of code calculates the derivative. It subtracts the current error from the past error to find the change in error.
Derivative = rate of change of error = current error – last error
Correction (D_fix) = Derivative scaled by proportional constant (Kd) = 1.0
derivative = error - lastError
lastError = error
D_fix = derivative * 1

## Slide 14: Putting it all Together
Each of the components have already been scaled. At this point we can simply add them together.
Add the three fixes for P, I, and D together. This will compute the final correction
In SPIKE Prime, we use % power so that the motors will be unregulated.
correction = P_fix + I_fix + D_fix
motor_pair.start_tank_at_power(int(40+correction), int(40-correction))

## Slide 15: Full Code
This is what you get if you put all these parts together.
We hope you now understand how PID works a bit better.
from spike import PrimeHub, LightMatrix, Button, StatusLight, ForceSensor, MotionSensor, Speaker, ColorSensor, App, DistanceSensor, Motor, MotorPair
from spike.control import wait_for_seconds, wait_until, Timer
from math import *
hub = PrimeHub()
color = ColorSensor('F')
motor_pair = MotorPair('A', 'E')
integral = 0
lastError = 0
while True:
error = color.get_reflected_light() - 50
P_fix = error * 0.3
integral = integral + error # or integral+=error
I_fix = integral * 0.001
derivative = error - lastError
lastError = error
D_fix = derivative * 1
correction = P_fix + I_fix + D_fix
motor_pair.start_tank_at_power(int(20+correction), int(20-correction))

## Slide 16: Key Step: Tuning The PID constants
The most common way to tune your PID constants is trial and error.
This can take time. Here are some tips:
  Disable everything but the proportional part (set the other constants to zero). Adjust just the proportional constant until robot follows the line well.
  Then, enable the integral and adjust until it provides good performance on a range of lines.
  Finally, enable the derivative and adjust until you are satisfied with the line following.
  When enabling each segment, here are some good numbers to start with for the constants:
    P: 1.0 adjust by ±0.5 initially and ±0.1 for fine tuning
    I: 0.05 adjust by ±0.01 initially and ±0.005 for fine tuning
    D: 1.0 adjust by ±0.5 initially and ±0.1 for fine tuning

## Slide 17: Evaluating Line followers
Proportional
Uses the “P” in PID
Makes proportional turns
Works well on both straight and curved lines
Good for intermediate to advanced teams  need to know math blocks
PID
It is better than proportional control on a very curved line, as the robot adapts to the curviness
However, for FIRST LEGO League, which mostly has straight lines, proportional control can be sufficient

## Slide 18: CREDITS
This lesson was created by Sanjay Seshan and Arvind Seshan for Prime Lessons
More lessons are available at www.primelessons.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.