## Slide 1: PROPORTIONAL Line FOLLOWER
BY SANJAY AND ARVIND SESHAN

## Slide 2: Lesson Objectives
Learn to create a proportional line follower
Learn how to calculate error and correction
Learn how to use variables and math blocks

## Slide 3: How Far Is the Robot From The Line?
Reflected light sensor readings show how “dark” the measured area is on average
Calibrated readings should range from 100 (on just white) to 0 (on just black)
Light Sensor Measured Area:
Line
Reading = 100
Reading = 0
Reading = 50
Reading = 25
Reading = 75

## Slide 4: Line Following
Computing an error  how far is the robot from a target
  Robots follow the edge of line  target should be a sensor reading of 50
  Error should indicate how far the sensor’s value is from a reading of 50
Making a correction  make the robot take an action that is proportional to the error. You must multiply the error by a scaling factor to determine the correction.
  To follow a line a robot must turn towards the edge of the line
  The robot must turn more sharply if it is far from a line
  How do you do this: You must adjust steering input on move block

## Slide 5: How do you make a Proportional Line Follower?
Pseudocode:
Compute the error = Distance from line = (Light sensor reading - Target Reading)
Scale the error to determine a correction amount. Adjust your scaling factor to make you robot follow the line more smoothly.
Use the Correction value (computed in Step 2) to adjust the robot’s turn towards the line.

## Slide 6: Challenge
Compute Error | 
Distance from line = (Light sensor reading - Target Reading) | 
Compute Correction | 
Scale the error to determine a correction amount. Use this to adjust power input on move block. | 
Apply Correction | 
Use the correction and a base power to control each motor. | 
error
error = color.get_reflected_light() - 50
correction = error * 0.3
motor_pair.start_tank(int(40+correction), int(40-correction))
# Note that the int function is used on the inputs to ensure that
# speed is an integer

## Slide 7: Proportional Line Follower
Part 1: Compute the Error
Our goal is to stay at the edge of the line (light sensor = 50)
Part 2: Apply the correction
The error in part 1 is multiplied by a Constant of Proportionality (0.3). This will be different for each robot/application. See slide 8 to learn how to tune this number.
from spike import PrimeHub, LightMatrix, Button, StatusLight, ForceSensor, MotionSensor, Speaker, ColorSensor, App, DistanceSensor, Motor, MotorPair
from spike.control import wait_for_seconds, wait_until, Timer
from math import *
hub = PrimeHub()
color = ColorSensor('F')
motor_pair = MotorPair('A', 'E')
while True:
error = color.get_reflected_light() - 50
correction = error * 0.3
motor_pair.start_tank(int(40+correction), int(40-correction))
# Note that the int function is used on the inputs to ensure that
# speed is an integer

## Slide 8: Key Step: Tuning the Constant
Note, the 0.3 constant in the previous slide is specific to our robot – you need to tune this value for yourself
This constant is called the Proportional Constant, or Constant of Proportionality
The most common way to tune your constant is trial and error.
This can take time. Here are some tips:
  Start with your constant as1.0 adjust by ±0.5 initially
  Adjust to a point where the controller is pretty smooth
  Adjust ±0.1 for fine tuning

## Slide 9: CREDITS
This lesson was created by Sanjay Seshan and Arvind Seshan for SPIKE Prime Lessons
More lessons are available at www.primelessons.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.