## Slide 1: PLAYING SOUND
BY SANJAY AND ARVIND SESHAN
This lesson uses SPIKE 3 software

## Slide 2: LESSON OBJECTIVES
Learn how to use the hub sound functions to play sounds

## Slide 3: SPEAKER FUNCTIONS
Used to play beeps out of the Hub.
You can set the volume of beeps
sound.volume(volume)
You can play a note of your choice for a particular duration. It is asynchronous, so use await if you want to wait.
await sound.beep(frequency=440, duration=500, volume= 100, …)
This function has a lot of parameters. You can find details in the Knowledge Base.
You can stop all noise from the hub by calling
sound.stop()
0-100
Frequency
Duration of beep in ms
(default value: 500)

## Slide 4: CHALLENGE AND SAMPLE SOLUTION
Set the speaker volume to 75%
Compose a short piece of music with 4 notes
Play it 4 times
from hub import sound
import runloop, sys
async def main():
sound.volume(75)
for i in range (4):
await sound.beep(400, 250)
await sound.beep(600, 250)
await sound.beep(800, 250)
await sound.beep(1000, 250)
sys.exit("Done")
runloop.run(main())

## Slide 5: CREDITS
This lesson was created by Arvind and Sanjay Seshan for Prime Lessons
Additional contributions by FLL Share & Learn community members
More lessons are available at www.primelessons.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.